## Choice LDO's

The 3.3V ON LDO's are small and cheap. Still can be controlled.
150mA should be sufficient to drive a number of external I2C devices that have for standard operations currents << 10mA

The maximal voltage for these LDO's are 5.5 V ( operational voltage, 6V absolute max )
To get some margin a 1N4448 ( 500mA ) is placed in front of all the LDO's
expected current < 300mA , .3 * 1.5 = .450 mW

need 1uF at the ouput / input

### Temperature allert .
The enable input of U1 is connected to the temperature allert output of the AT30TSE752. This is done via a resistor so the function can be "removed",

## I2C circuits

### PCA9517A buffer: (obsolete)
Was a consideration for only 2 I2C busses.
If the power on the external buffer is switched off the I2C lines will pull down and it will not be possible to control the MCP23009.
It is important that the LDO's and the I2C buffers are controlled by the same line, both high.

The PCA9571 can only drive 400pF. Consider to use in series a 82B715D bus extender.
But the 82B715D has no disable function. Didn't find a device that can do both.

PCA9515 was also considered as this has only one power supply but is an "old" device .
Check if the PCA9571 to replace the level shifter on the analogue board.

### P82B715
With V 0.4 it is assumed there are three I2C busses on X1.
The SCL_L is used to control the devicies on the card.

SCL1in and SCL2in are the busses to communicate with the remote sensors.
If the power supply on these remote sensors are off , the SCLXin , SDAXin lines will be pulled to zero. The "master" that controls these lines should be able to cope with this.

The P82B715 is able to drive a high capacitive load on its LX and LY outputs but has no disable function.

other option would be TCA4311A or PCA9510A. But these can only drive 400pF altough intended to drive a back plane. These support hot swappable what is what we do.
## PCA9557
pin assignment is not yet fixed. Depends on the layout.
Only IO0 will be fixed to GPIO as this is an open drain. There is a pull up resistor R9

# Programming ID
R10 and R11 are there to make it possible to lock and unlock the AT30TSE752 flash. This should contain ID information about this board. Connections have to be made via TP0 and TP1 these have a kind of press fit for std pin headers ( square pins)