SOLID Humidity Sensor

## version history
version : 20161117 V1.0 initial version of schematic and board layout
not yet for production (
Last saved date : 17 Nov 2016 15:20:35

version nov 2016 V0.1 version without layout. not documented

## introduction

In this folder you find information for the assemblage the humidity sensor circuit for the SOLID scientific project.

The PCB is created by the Eagle software form CADSoft ( Autodesk)

This project is related to the SOLID temperature sensor.

Dimension of the board is ~ 11.5 x 16.5 mm

On the board there is a voltage regulator but normally is not used and the resistor R1 of 0 ohm has to be mounted.
In that case the max voltage is 3.6 V . But nominal 3.3 V.
In case the LDO is used the max voltage is 5.5 V. But the I2C lines are still between 3.3 and 0 V.

There are no pull ups on the I2C line. Standard is 100 kHz I2C bus.

The address is BE read , BF write

For more details see the data sheet of the humidity sensor in the doc directory

The connector used is of the family micro-match 6 sockets . The corresponding wire pin connector is 7-215083-6 ( Farnell[1] order code 149068 )
[1] Mouser is in general cheaper in big quantities

If only 4 wires are connected it is also possible to place the the 7-188275-4 (Farnell 3784710) , 4 pins socket . Same as used for the SiPm board.

7-215083-4 ( Farnell 149032 )
### technical contact information:
W. Beaumont Universiteit Antwerpen
wim.beaumont@uantwerpen.be
office phone 0032 3 256 3558 , in case of no answer please drop an e-mail

### Commercial contact information:

## Design sources / info

- SOLID_HSENSOR_sch.pdf SOLID_HSENSOR_brd.pdf pdf files of the design.
- SOLID_HSENSOR_info.odt this file.
- SOLID_HSENSOR_info.pdf this file in pdf format
- SOLID_HSENSOR_bom.csv/ods bill of material
- diretory doc : data sheet .