SOLID Humidity Sensor

## version history
version : 20161117 V1.2 layout version used for PCB production
Last saved date : 17 May 2017 17:02:45
version : 20161117 V1.0 initial version of schematic and board layout
not yet for production (

version nov 2016 V0.1 version without layout. not documented

## introduction

In this folder you find information for the assemblage the humidity sensor circuit for the SOLID scientific project.

The PCB is created by the Eagle software form CADSoft ( Autodesk)

This project is related to the SOLID temperature sensor.

Dimension of the board is ~ 11.5 x 16.5 mm

On the board there is a voltage regulator but normally is not used and the resistor R1 of 0 ohm has to be mounted.
In that case the max voltage is 3.6 V . But nominal 3.3 V.
In case the LDO is used the max voltage is 5.5 V. But the I2C lines are still between 3.3 and 0 V.

There are no pull ups on the I2C line. Standard is 100 kHz I2C bus.

The address is BE read , BF write

For more details see the data sheet of the humidity sensor in the doc directory

The connector used is of the family micro-match 6 sockets . The corresponding wire pin connector is 7-215083-6 ( Farnell[1] order code 149068 )
[1] Mouser is in general cheaper in big quantities

If only 4 wires are connected it is also possible to place the the 7-188275-4 (Farnell 3784710) , 4 pins socket . Same as used for the SiPm board.

7-215083-4 ( Farnell 149032 )
### technical contact information:
W. Beaumont Universiteit Antwerpen
wim.beaumont@uantwerpen.be
office phone 0032 3 256 3558 , in case of no answer please drop an e-mail

### Commercial contact information:

## Design sources / info

- SOLID_HSENSOR_sch.pdf SOLID_HSENSOR_brd.pdf pdf files of the design.
- SOLID_HSENSOR_info.odt this file.
- SOLID_HSENSOR_info.pdf this file in pdf format
- SOLID_HSENSOR_bom.csv/ods bill of material
- diretory doc : data sheet .

## Status

### PCB

The PCB was submitted together with the T-Sensor board on 1 PCB layout.
For more details see SOLID_TSensor info.
It turned out that the foot -print for the temperature sensor was mirrored. The lib that was taken from the web was not checked.
Still one sensor was placed ( with the housing to the PCB ) and connected with wires. This is not a very reliable method.
Still it was possible to operate the sensor so there are no mistake in the schematic. ( only the version without the regulator is tested)

A new layout version with the correct food-print of the HTS221 sensor is ready. It has the same dimensions but the components are mirrored in respect to the connetor.

For commercial reasons a panel was made with several temperature probes and humidity probes PCB's based on the

### Software

A class to readout the hts221 board exist:
https://developer.mbed.org/users/wbeaumont/code/HTS221tst/

Tested is the readout of the temperature and the humidity as well the chip ID.