## Choice LDO's

The 3.3V ON LDO's are small and cheap. Still can be controlled.
150mA should be sufficient to drive a number of external I2C devices that have for standard operations currents << 10mA

## PCA9517A buffer:
If the power on the external buffer is switched off the I2C lines will pull down and it will not be possible to control the MCP23009.
It is important that the LDO's and the I2C buffers are controlled by the same line, both high.

The PCA9571 can only drive 400pF. Consider to use in series a 82B715D bus extender.
But the 82B715D has no disable function. Didn't find a device that can do both.

PCA9515 was also considered as this has only one power supply but is an "old" device .
Check if the PCA9571 to replace the level shifter on the analogue board.