Changes

data 27 July 2016

corrected voltage set resistor values for the LDO's .
Changed the symbol and case for the pol. Capacitors around the LDO's
removed the I2C GPIO device
connected the power enable of the positive and negative LDO's ( removed one resistor to ground)
– added resistors to get the board also working without control

removed the temperatured alert
-- input for digital card or temperature is monitored via the I2C ??

amplifier
corrected the DC shifter. Connections where wrong ,
calculated resistor values for the level shifter added to the schematc .
removed the parallel capacitors at the input .

bias
R17 ( HV bias) will be placed by default. HV range increase by .5 V

added the GPIO connected GPIO to specific functions , 1 GPIO still not assigned

To do :

oct 06
added some capacitor.
rename input / output nets to be compatible with digital board
rename trim voltage signals to the i/o name so all should be consistent module D0 , ip0 , in0, trim0 ,op0 on0

Jan 2017
improvements / corrections

- fuses are to close to the connector so hard to replace (corrected inV1.3 )
- need a jumper on the power on line to power the board if no ADC board is connected.
  - also a 1.8 input or resistors from the 5 V.
- silkstreen W.Beaumont and Universiteit Antwerpen are not on the bottom silk screen( corrected layout V1.3 )
- LDAC and eeprom address lines to a socket so easy to connect. (done V 1.3)
- Solder resist mask DIN 61412 are not correct.( corrected in layout V1.3 )
- Added at input and output scotky diodes .on the power ( in V1.3 )
- added zener diode on the 1.8 V input ( done V1.3)
- added protection diodes between 1.8 and 0 V to protect ADC inputs ( done V1.3 , layout not done )
- put back ( ver 1.2) the connections of the input according the quotation version ( what was finally produced) done v1.3