Changes

data 27 July 2015

corrected voltage set resistor values for the LDO's .
Changed the symbol and case for the pol. Capacitors around the LDO's
removed the I2C GPIO device
connected the power enable of the positive and negative LDO's ( removed one resistor to ground)
– added resistors to get the board also working without control

removed the temperatured alert
-- input for digital card or temperature is monitored via the I2C ??

amplifier
corrected the DC shifter. Connections where wrong ,
calculated resistor values for the level shifter added to the schematc .
removed the parallel capacitors at the input .

bias
R17 ( HV bias) will be placed by default. HV range increase by .5 V

added the GPIO connected GPIO to specific functions , 1 GPIO still not assigned

To do :